### Damocles 2404i: SNMP DI/DO over IP

24 digital inputs, 4 relay outputs, Web interface. Industrial DIN rail housing. M2M support (SNMP, XML, Modbus/TCP). DI can be used as a meter pulse counter.

The Damocles 2404i is an IP device (snmp / web relay) with 24 digital inputs (dry contacts) and 4 relay outputs, mountable on a DIN rail. One temperature probe can be also connected.

Provides a Web interface, M2M communication (SNMP, Modbus/TCP, XML/HTTP).

When a dry contact input changes value, the Damocles sends an email with customizable text and/or a SNMP trap. Alerts can be delayed by a defined time (for example, to send an email if a freezer door stays open for more than 5 minutes).

Damocles 2404i is typically used as a remote relay control to switch on or off other devices (snmp web relay, remote restart or remote relay).

Box-2-Box mode:

Changes at a dry contact input of one device (A) are sent over the network (SNMP Trap) and reflected at the relay output of the other device (B). The Damocles 2404i can react to changes at the inputs of another Poseidon or Damocles unit (without any additional software).

Example: 	Too high temperature in the datacenter (measured by Poseidon 3266) turns on a warning red light in the IT department in another building (relay output of Damocles 2404i).

- Online demo: http://damocles-2404.hwg.cz/values.xml

- Ethernet: RJ45 (10BASE-T)

- WEB: Built-in web server, GUI for configuration

- Digital Inputs: 24 digital inputs (dry contacts) with pulse counters

- Digital Outputs: 4 relays (24VDC)

- Sensors: 1 Temp-232 temperature probe (RS-232 interface)

- M2M communication protocols: SNMP, XML, Modbus/TCP

- Reaction to changes at the input: SNMP trap, Email (customizable text)

- Box-2-Box mode: Outputs are activated by alerts from other devices (Poseidon / Damocles)

- HWg-PD Trigger: Alert redirection to SMS, Pop-Up, shutdown PC, ..

- HWg-PDMS: Logging of values, graphs, export to MS Excel

- CapTemp software: Visualization in a map, control of outputs, alarm redirection to SMS

# Text boxes

Keywords:

Damocles 2404i, SNMP DI DO, meter pulse counter, remote relay control, snmp web relay

M2M IP relay, relay control remote, remote restart, remote relay, xml relay, modbus tcp relay, remote reboot, box-2-box relay, dry contact email