### Poseidon 3268: WEB thermometer & I/O with SNMP

Ethernet temperature / humidity monitoring with 2 relay outputs and 4 dry contact inputs (Web, SNMP, and E-mail). Output relays can be controlled over the Web.

The Poseidon 3268 is a unique IP device featuring 2 relay outputs (NO/NC). The Poseidon 3268 measures temperature and humidity, and monitors four dry contact inputs. 
Digital inputs (for dry contacts) can be used for connecting door contacts, smoke detectors, water flood detectors, and 110/230V AC power supply failure detectors.

Relay outputs can control cabinet heating / cooling using a local probe (“thermostat” / “hygrostat” function).

The outputs can be controlled remotely over IP (server restart with a PowerEgg unit, or opening the cabinet door remotely).

When a dry input contact is closed, the Poseidon sends an e-mail or a SNMP trap. The alert can be postponed by a defined time (an e-mail is sent if a cabinet door has been open for more than 5 minutes).

With the PD Trigger software, alerts can be redirected to SMS or processed according to the PD Trigger rules (set/clear a remote relay over IP, show a pop-up message in Windows).

In a typical application, Poseidon 3268 controls the environment in a cabinet that is equipped with a fan. Critical temperature or door being opened alerts are sent to a central system. The Poseidon 3268 is also frequently used to restart a server or A/C unit remotely.

Note: 	To get started, we recommend ordering the “Poseidon 3268 Tset” that contains a power supply adaptor, a temperature sensor, a door contact, user manual and a CD.

- Online demo: http://poseidon-3268.hwg.cz/values.xml

- Ethernet: RJ45 (10BASE-T)

- Web: Built-in web server

- Sensors: 1xRJ11 1-Wire (max. 5 temperature / humidity probes)

- Digital Inputs: 4 digital inputs (dry contact) 
(door contact, smoke detector, 11/230VAC supply detector, water leak detector, cooling fan failure detector)

- Digital Outputs: 2 relays (24VDC)
(air conditioning, server power, warning horn / light tower)

- Local built-in functions: Control of output using an digital input value or a sensor value (“thermostat” / “hygrostat” mode)

- Alerts (value out of defined safe range): SNMP trap, E-mail

- M2M communication protocols: SNMP, XML

- Support for programmers: HWg SDK

- Supported software

  - HWg-PD Trigger: Alert redirection to SMS, Pop-Up, shutdown PC, ..

  - HWg-PDMS: Logging of values, graphs, export to MS Excel

  - CapTemp: Visualization on a map, control of outputs, alarm redirection to SMS

  - Third-party SNMP software

# Text boxes

Keywords:

Web relay, web enabled thermostat, SNMP I/O, web thermometer, MS Excel reporting

dry contact, snmp relay, digital thermostat, humidity controller, ip relay, hygrometer, racks room, environmental monitoring system, Nagios, Zenoss, Cacti, HP OpenView