### I/O Controller 2: Full serial port and I/O to Ethernet

I/O Controller 2 connects a full RS-232(485) serial port and digital I/O to the Ethernet. Two devices can be connected back-to-back to tunnel the serial port and I/O over the network.

Digital inputs are used to connect external relays or pushbuttons. Eight outputs can be connected to external relays. I/O can be controlled over the Web, Modbus/TCP, or Telnet NVT protocol.

The serial port can be accessed using the Telnet protocol, or redirected to a virtual serial port in Windows (e.g. COM 27). The full serial port supports all 9 signals and ensures correct operation.

As an interesting application, the serial port and digital I/O can be extended (“tunneled”) between two I/O Controller units over a LAN IP network.

Other applications include connecting peripherals (RS232 barcode reader, pushbuttons, status indicators) to a central system in manufacturing environments.

- Ethernet: RJ45 (100BASE-T / 100 Mbit/s)

- Configuration: Web, Telnet

Inputs: 8 digital inputs (for dry contacts)

Outputs: 8 digital outputs (open collector)

- Serial interface: 1x full RS-232 or RS-485 serial port

- Full RS-232 serial port: RxD, TxD, GND, CTS, RTS, DSR, DTR, RI, CD / 115.200 Bd.

- Box-2-Box mode: Two units can be connected back-to-back over the network and tunnel the I/O and the serial port.

- M2M protocols: http, Modbus/TCP, Telnet, TCP Server, TCP Client/Server

- Support for programmers: HWg-SDK

- Free HW VSP software: Virtual serial port for Windows (NT service, x64 systems). Supports up to 100 remote serial ports. HW VSP is the world's most popular virtual serial port for Windows!

# Text boxes

RS-232 devices

- Barcode reader

- RFID reader

- Serial printer

- LCD display

- Modem interface

- Access system

Keywords:

I/O Controller 2, full serial port, serial port and I/O to Ethernet, RS-232/485 to IP, Modbus/TCP, serial terminal server, com to ethernet, full rs-232 over LAN

serial converter, com port to ethernet, ethernet com port, full serial port to IP, Device server with IO, DI & DO to Ethernet, free virtual serial port,