### HWg-STE PoE: SNMP thermometer

HWg-STE PoE is IP enabled web thermometer with Email alerts and SNMP. Measure temperature and humidity with two external probes. Powered over Ethernet or from wall plug adaptor.

The HWg-STE PoE web thermometer is configured using a built-in web server. If the temperature (humidity) exceeds a specified threshold, an e-mail alert is sent. Free windows software HWg-PDMS for graphical overview and MS Excel export included.

The HWg-STE IP thermometer is fully SNMP compatible.

PoE temperature monitor, E-mail alert to overheating or temperature drop

Windows software, AC power adapter and temperature probe included

Simple installation, supports DHCP & PoE (IEEE 802.3af)

Typical applications include remote monitoring the temperature of equipment, computers or disk arrays, or monitoring HVAC operation.

Online demo: http://hwg-ste.hwg.cz

- Ethernet: RJ45 (100BASE-T)

- Power: PoE (IEEE 802.3af) or wall plug adaptor (included in delivery)

- WEB: Built-in Web server

- Sensors: 1xRJ11 1-Wire (max 2 temperature / humidity probes)

- M2M communication protocols: SNMP, XML

- Alerts (value out of defined safe range):  E-mail

- HWg-PDMS software: Logging of values, graphs, export to MS Excel

# Text boxes

Keywords:

HWg-STE PoE SNMP thermometer, PoE temperature monitor, PoE thermometer, power over ethernet thermometer, IEEE 802.3af, temperature monitor, snmp temperature, computer room, server monitoring

PoE thermometer, PoE temperature sensor, PoE, snmp, email alert, poe temperature, temperature report, poe humidity