### HWg-SH3: Cabinet IP access system with RFID & SNMP

RFID cabinet access control system with SNMP interface. User database configurable over the Web. Can be used as central or stand-alone system. Remote monitoring over Email and SNMP.

HWg-SH3 is an autonomous RFID cabinet access control system. The database of authorized tags/cards can be managed remotely over the Web.

HWg-SH3 uses a local RFID reader and controls the front and rear doors of a cabinet.

The unit can be used as a stand-alone offline solution independent on any software. HWg-SH3 can be also used in online mode with access authorization against the HWg-DCD application.

You can open the doors over the Web

RFID tag database can be edited over the Web

A door contact for detecting the state of the door (open/closed) can be connected

Uses a external RFID reader (support 127 kHz or 13.5 MHz)

Detects entry with a key / violent entry / cable disconnected

Standalone operation – Door can be opened with: RFID tag/card, key, Web interface

Online with HWg-DCD – Door can be opened with: SMS access code, HWg-DCD admin interface, LAN RFID terminal (e.g. located near the entrance to the room)

HWg-SH3 is typically used in a remote cabinet, rack or box, which may be accessed by a few authorized users only. Authorized users can be changed remotely over the Web interface.

HWg-SH3 has the advantage of easy installation and internal tag database.

- Ethernet: RJ45 (10/100 Mbit)

- WEB: Built-in Web server

- Protocols: SNMP, Syslog, SMTP

- Electronic Swing Handles: Two HWg-SH1 (Southco H3-EM - Electronic Locking Swinghandle) supported.

- Inputs: 2 digital inputs for door contacts (front/back door)

- RFID reader: RS-232 / Wiegand for connecting a RFID reader

- Physical features: Rack mount (on the side), dimensions: 96 x 78 x 30 [mm]

- LAN interface: Secure communication with the HWg-DCD application running on a central server

- Compatible software: HWg-DCD for access control (remote control of rack doors) for data centers

# Text boxes

Keywords SH3:

HWg-SH3, IP access control system, RFID door lock, datacenter swing-handle, cabinet access system, RFID ACS, SNMP

remote access, rack door remote control, web snmp, remote access system, southco H3-EM, dirak swing handle, emka lockagent, accesscontrol, access security, datacenter access system, cabinet access system, rack access control system, card access system, mifare, network ACS, WEB access control system