### IP Relay HWg-ER02b: Web relay + full serial port over IP

Ethernet relay, DIN rail, Web interface. Features 2x DI (dry contact input), full RS-232/485 serial port, and 2x DO (relay output, 230V/16A). It is controlled over the web or Modbus/TCP.

Relay outputs can directly switch 230V/16A AC mains, dry contact inputs can be used e.g. for buttons. The device features a full RS-232/485 serial port for connecting e.g. a RFID or barcode reader. Industrial model, fits on a DIN rail.

Ethernet I/O can be controlled over the Web, Modbus/TCP, or Telnet NVT protocol. The full serial port supports all 9 signals and ensures maximum compatibility.

The serial port can be redirected as a virtual serial port to Windows (e.g. COM 27), or controlled using a Telnet protocol.

Two products can be connected back-to-back to extend (“tunnel”) the serial port and I/O over a LAN.

Typical applications include opening a remote gate over a LAN (relay output) and connecting a RFID card reader (RS-232).

- Ethernet: RJ45 (100BASE-T / 100 Mbit/s)

- Configuration: Web, Telnet

- Inputs: 2 digital (dry contact) inputs

- Outputs: 2 NO/NC digital (relay) outputs, rated 230V/16A

- Serial interface: 1x full RS-232 or RS-485 serial port

- Full RS-232 serial port: RxD, TxD, GND, CTS, RTS, DSR, DTR, RI, CD / 115.200 Bd.

- Box-2-Box mode: Two units can be connected back-to-back over the network and tunnel the I/O and the serial port.

- M2M protocols: http, Modbus/TCP, Telnet, TCP Server, TCP Client/Server

- Support for programmers: HWg-SDK

- Mechanical: 145 x 90 x 45 mm, wall-mountable, fits on a DIN rail

- Free HW VSP software: Virtual serial port for Windows (NT service, x64 systems). Supports up to 100 remote serial ports. HW VSP is the world's most popular virtual serial port for Windows!

remote power switch		2400

power control				2400

relay switch				4400

remote control relay		390

web relay				480

Ethernet relay			590

remote power control		390

lan relay				50

| ip relay | 3 600 | Nízká | 0,83 US$ | 0 % | ÚČET |
| --- | --- | --- | --- | --- | --- |
| remote relay | 260 | Vysoká | 0,53 US$ | 0 % | ÚČET |
| serial converter | 260 | Střední | 1,65 US$ | 0 % | ÚČET |
| com port to ethernet | 30 | Vysoká | 2,57 US$ | 0 % | ÚČET |
| free virtual serial port | 140 | Nízká | 0,34 US$ | 0 % | ÚČET |
| ethernet com port | 50 | Střední | 0,92 US$ |  |  |

# Text boxes

Keywords:

IP Relay, remote power switch, web relay, power control, Ethernet relay, lan relay, full serial port, serial converter, rs-232 over Ethernet, remote relay, Ethernet IO

Digital I/O transport, relay switch, remote io, serial over ip, serial to ip, rs232 to ethernet, serial to Ethernet, ethernet controlled relay, relay switch, remote control relay, network relay, relay over network, remote relay, power controlled ethernet, remote power control, relay Modbus-TCP, free virtual serial port, rs-485, DIN relay,

Klíčová slova:

IP Relay HWg-ER02a, vzdálené relé, web relé, ovládání napájení, Ethernet relé, síťové relé, plný sériový port, sériový převodník, RS-232 přes Ethernet, vzdálené relé

přenos I/O, Relé výstup, RS-232/485 na IP, Modbus-TCP, com na ethernet, plná rs-232 po LAN, rs-485 na Ethernet, sériový konvertor, com port na ethernet, ethernet com port, plný sériový port na IP, virtuální sériový port zdarma, relé ovládané po ethernetu, din relé, síťové relé, relé ovládané po síti