### HWg-Trigger: Event management software (IF-THAN)

HWg-Trigger is an event management software for Windows. Detects disconnected sensors, values out of allowed range, or pressed buttons. A condition triggers an action. For example, a text message (SMS) is sent to several numbers, a relay output is activated over the network, a Windows application is started, or a warning message is displayed.

A “Condition” (event) and its assigned “Action” form a “Rule”. Up to 90 rules can be added to the application. For each rule, a repetition interval can be specified. Each rule can be tied to an IP address (e.g. to distinguish if the notebook with the application is connected “at home”, “in the office”, or at a “public place”).

Monitored conditions (input events)

- Device disconnected – Device is unavailable for a certain period of time

- Sensor disconnected – Device is available but at least one of its sensors is disconnected

- Sensor outside SafeRange – At least one sensor reading is outside of the specified range

- Sensor value – Sensor reading is higher than / less than the configured value

- Failure of listed device – A device on the list is unavailable

- Sensor alert (SNMP Trap)

- Device restart (SNMP Trap)

Available actions

PC: Display a pop-up window, play a sound, start an application, start a service, shut down the PC

Over the network: Turn on/off a remote relay output, send a text message (HWg-SMS-GW)

With a GSM modem connected: Send a SMS with alert text

Typical applications:

- Display a warning whenever 1 or more out of 15 devices is not responding, or has a sensor in alarm.

- If the temperature in room A is high, send an e-mail to Peter. If the temperature in room B is high, send a text message to Peter and to Thomas.

- When a button is pressed (Digital Input of a Poseidon unit), activate 4 relay outputs over IP (Digital Outputs of various Poseidon or Damocles units).

- Watch 10 sensors at 3 devices. Send a SMS through HWg-SMS-GW whenever any of the sensor readings is outside of the specified range.

Basic features

Operating system: Windows (NT service)

Trial version: 30 days

Data input: SNMP Trap, PING, XML polling

Compatible devices: Poseidon, Damocles, HWg-WLD, HWg-PWR

Data processing: Condition > Action

License

HWg-Trigger: 30-day trial version (fully functional)

HWg-Trigger: Unrestricted commercial version

# Text boxes

Keywords:

HWg-Trigger, condition, event, forward to SMS, IP sensor monitoring, SMS alert, activate relay, detect device failure, detect disconnected sensor, detect sensor value, LAN device watchdog, MS Windows alert software